## Slide 1: Cardiac Simulations with Sharp Boundaries Preliminary Report
Shuai Xue, Hyunkyung Lim, James Glimm
Stony Brook University

## Slide 2: The Context
Fenton and Cherry propose low voltage defibrillators. Reduces pain and stress to patient
Simulations to design/evaluate low voltage effects are needed
Voltage is injected into intracellular space

## Slide 3: A Model
Heart chamber has thin walls: 2-15 mm
Wall is composed of fibers (like a ball of string)
Conduction is 5X faster in fiber direction
Electrical current propagates by diffusion, 5X faster in fiber direction. So the diffusion tensor is anisotropic
Thin walls means that the simulation is dominated by boundary effects

## Slide 4: Bidomain Models
Because defibrillation voltage is deposited into intracellular space, we need to model separately the voltage there and the voltage in the fibers.
Fibers are much smaller than the computational grid, so typical cell has two voltages, one for fibers in it and one for intracellular space.
This is called a bidomain model
It is a goal of present project.
How much voltage in the intracellular space is needed to “restart” a fibrillating heart?

## Slide 5: A Numerical Analysis Perspective
Two key issues:
Fast reaction source term
Diffusion equation for propagation of voltages
Fast reaction: focus of most of numerical cardiac community. Many models of
varying degrees of complexity and validation, and serving different goals
Diffusion equation has sharp boundary (no conduction outside of heart tissue), thin walls, curvilinear boundary.
Diffusion equation can also distinguish conduction fiber voltages from intracellular voltages (in bidomain models)
Physiological defects (i.e. dead tissue), blood vessels add fine scale structure, difficult to resolve numerically. Is this important? I suppose so.

## Slide 6: Typical resolution
Delta x = ~ 0.1 -- 0.2 mm; Delta t ~ 0.01 -- 0.02ms
Heart wall = 2 -- 15 mm
Large blood vessel = ~ 5 mm
Wall model (phase field) = 4 delta x = 0.4-0.8 mm
Occupies 5% to 80% of heart wall
Goal: sharp boundaries, 0 Delta x at wall
Cost of mesh refinement for present explicit algorithm: A refinement factor of 2 costs 25 = 32 (~ Delta x3 X Delta t2 = Delta x5)
Cost of mesh refinement for proposed implicit algorithm: 23 = 8 (Delta x3)
[costs for parabolic step; calculation of currents has distinct scaling, due to small time steps and subcycling]
Benefits: improve speed, eliminate wall effects, resolve large blood vessels [needs data not presently available], add bidomain feature

## Slide 7: Proposed Algorithm
Bidomain
Sharp boundaries
Implicit
Ability to resolve large blood vessels
Current work: Accept the Fenton reaction source term model, concentrate on the diffusion equation

## Slide 8: Diffusion equation
The diffusion equation is a parabolic equation, the essence of which is the associated elliptic problem (steady state parabolic).
Optimal methods should
1. allow sharp boundaries
2. be second order convergent
3. be solved implicitly, to avoid stability requirements for small time steps (accuracy requirements remain)
Possible methods
Embedded Boundary Method: should do 1+2+3
Immersed Interface Methods: should do 1+2+3
Phase field method: Fails 1, 2; 3 should be possible but not used
Buzzard et al: Attempts 1, but method unclear and undocumented
Immersed Boundary Method Fails 1, 2
Conclusion: EBM and IIM are best suited.
We select EBM (due to local experience) and start with first order convergence

## Slide 9: Computational Kernel
Elliptic solution (Laplacian u = f; f given and the problem is to find u)
Basic step in parabolic solution, in the propagation of the electrical signal
Method of embedded boundary (Colella and others). Add additional degrees of freedom to solution in the cut cell. Present work is 1st order accurate. Method should extend to 2nd order accurate. Errors reported in norm, i.e. sup norm. This is because of major problem with errors at boundary, which will be strongly present in the norm. Because these errors are controlled, solutions should be accurate up to the boundary, with no “numerical boundary layer”
Anisotropic case is new work

## Slide 10: Current Status
(Better than) first order convergence in Linftry , L1, l2 norms, isotropic and anisotropic cases
Note: Linfty convergence is proof that sharp boundaries are working correctly
Method should allow second order convergence

## Slide 11: Isotropic Cylinder convergence order = 1.7
Chart: 
| -0.69897000433601875 | -1 | -1.3010299956639813 | -1.6020599913279623 | -1.9030899869919435
 | -1.5046 | -2.3127 | -2.807 | -3.2469 | -3.5674

## Slide 12: Isotropic Sphere Convergence order = 1.5
Chart: 
| -0.69897000433601875 | -1 | -1.3010299956639813 | -1.6020599913279623 | -1.9030899869919435
 | -1.2038 | -1.9412 | -1.7471 | -2.7378 | -3.0251

## Slide 13: Anisotropic Sphere Convergence order = 1.3
Chart: 
| -0.69897000433601875 | -1 | -1.3010299956639813 | -1.6020599913279623
 | -2.0154 | -2.3522 | -2.7123 | -3.1118

## Slide 14: Anisotropic Sphere Convergence order = 1.4
Chart: 
| -0.69897000433601875 | -1 | -1.3010299956639813 | -1.6020599913279623
 | -2.4534 | -2.9458 | -3.2903 | -3.7286

## Slide 15: Anisotropic Sphere Convergence = 1.4
Chart: 
| -0.69897000433601875 | -1 | -1.3010299956639813 | -1.6020599913279623
 | -2.6222 | -3.1117 | -3.4589 | -3.9156

## Slide 16: Plans
Install into parabolic solver and into the Flavio-Cherry code
Benchmark and test.
Write paper based on this work
Add bidomain model
Draw conclusions regarding minimum defibrilator voltage, comparing new and prior codes.
Write a second paper
Solve problems with fine scale structure, if this is important physiologically (blood vessels, etc.)
Write a third paper
At some point, improve elliptic solver to second order